## Slide 1: Architecting Energy-efficient STT-RAM Based Register File on GPGPUs via Delta Compression
Hang Zhang, Xuhao Chen, Nong Xiao, Fang Liu
State Key Laboratory of High Performance Computing,
College of Computer,
National University of Defense Technology, China

## Slide 2: Overview
Background
Motivation
Design Details
Experimental Evaluation
Conclusion

## Slide 3: The Processing Engine in Big Data Era
GPGPU (General Purpose Graphic Processing Unit) has been widely employed
  Deep Learning
  Datacenter
  Supercomputer
“We also implemented a distributed version of AlphaGo that exploited multiple machines, 40 search threads, 1,202 CPUs and 176 GPUs” – Nature, 2016
However, energy-efficiency of GPUs become critical
  NVIDIA Tesla K80, 300W
  Core i7-980X Extreme Edition, 130W
  DOE supercomputer, 20MW

## Slide 4: GPGPU Architecture (GTX 480)

## Slide 5: GPU Architecture
SIMT architecture: Single Instruction Multiple Threads
  thousands of threads running together
  threads operates on different data
  hiding long memory access latency
Register file with large capacity
  save the contexts of threads
  512KB per SM (streaming multiprocessor) on NVIDIA K80
  constrain how many threads concurrently running
A register read/write operation from a warp
  32 threads / warp
  32 * 32 bit = 1024 bit

## Slide 6: SRAM is the bottleneck
Energy-efficiency of the register file
  conventionally built with high leakage SRAM
  consume a great portion of GPU total Energy, 15-20%
  Impediment for scaling up GPUs in future generation
High Leakage SRAM
  high leakage power consumption
    escalated leakage power as technology scales
  low density, e.g. 137F2
6T SRAM

## Slide 7: To combat SRAM leakage
STT-RAM (Spin Transfer Torque magnetic RAM)
  near zero leakage power
  high density, 6-37 F2
  good scalability, 1x nm
  good endurance, 10^15
Building STT-RAM GPU Register File
  R.F. and shared memory [HPCA’13], distributed buffer[DAC’15] , MLC STT-RAM [ASP-DAC’15]
  Achieve near-zero Leakage
However, writing STT-RAM cells becomes a problem
  high write energy consumption
  long write latency

## Slide 8: Design Goal
Prior proposals still suffer from
  performance degradation
  high dynamic energy consumption
Our goal
  leverage value similarity in SIMT architecture
  propose a lightweight compression framework to mitigate STT-RAM writes
  redesign a centralized write buffer for better utilization

## Slide 9: Register Value Similarity
Value similarity between successive register requests
  many thread-specific local variables, threadID
  some local variables are assigned similar
  input data arrays has a very narrow dynamic range
Register value similarity profiling
ISCA’15 Warped-compression: enabling power efficient GPUs through register compression
1. 79% of the registers are categorized as not random
during non-divergent execution phase
2. Compression algorithm can be effective

## Slide 10: A lightweight compression framework
Base-Delta-Intermediate (BDI) compression
  lightweight: 1 cycle compress/decompression
  high compression ratio: when data are similar
    Value similarity on SIMT architecture
If a data word can be compressed
  Base: first data chunk
  Delta: difference with base
  Intermediate

## Slide 11: Write driver enhancement
Fine Grained Write Driver Control
  32 groups for 1024-bit register entry
  Enable signals from the compression engine
Notes: 1. The write driver is redesigned to enable a fine-grained access control on how many of STT-RAM bits can be read/write at the same time.
2. To minimize the control complexity, a bits group of 32-bit is controlled together as a unit.
3. The signals from the compression engine are fed in as the control enabler.

## Slide 12: Centralized Write Buffer
Prior SRAM buffer design
  Each bank has its own write buffer
A
Bank1
Buffer1
Bank2
Buffer2
Bank3
Buffer2
A
B
Bank1
Bank1
Conflict!
Register Requests
Under utilization

## Slide 13: Centralized Write Buffer
Bank1
Buffer1
Bank2
Buffer2
Bank3
Buffer2
A
B
Bank1
Bank1
Register Requests
Buffer
Our proposed design
  A centralized write buffer shared by banks

## Slide 14: Centralized Write Buffer
Buffer
A
B
Our proposed design
  A centralized write buffer shared by banks
Buffer
A
Bank1
Bank2
Bank3
A
B
Bank1
Bank1
Register Requests
Buffer
Centralized writer buffer
  Better utilization
  Smaller total capacity (SRAM)

## Slide 15: Relaxed retention time STT-RAM cells
Chart: Write Pulse Width (ns)
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
10 years | 248.2682 | 173.7877 | 148.9609 | 136.5475 | 129.0994 | 124.1341 | 120.5874 | 117.9274 | 115.8585 | 114.2034
1sec | 158.5136 | 110.9595 | 95.1082 | 87.1825 | 82.4271 | 79.2568 | 76.9923 | 75.294 | 73.973 | 72.9163
10ms | 87.6926 | 61.3848 | 52.6156 | 48.2309 | 45.6002 | 43.8463 | 42.5935 | 41.654 | 40.9232 | 40.3386
Operating Point
Write current goes down with reduction in retention time
Retention Time of STT-RAM | Write Latency @ 700Hz
10 Years | 5.5 cycles
1 second | 3 cycles
10 millisecond | 1.5 cycles
Retention Time
10ms retention time equals 7000000 cycles on GPUs and is far more than 789 cycles (inter-access distance)

## Slide 16: Experimental Evaluation
Hardware Setup
  GPGPUSim simulator
  Nvsim
  NVIDIA GTX 480 architecture

## Slide 17: Evaluation: Register File Energy
Our proposed design consume only 37.4 % register file energy compared to the baseline on average.

## Slide 18: Energy Breakdown
Bar 1 is Base, Bar 2 is WB, Bar 3 is STT+BDI
1.STT-RAM can effectively cut off leakage energy
2. Compression is good at reducing dynamic energy

## Slide 19: GPU Performance
Our scheme can achieve near 99% performance of the SRAM baseline

## Slide 20: Conclusion
Register files on GPU becomes the key design consideration for future GPU architecture.
STT-RAM is a promising candidate for building GPU register files, if write operations are optimized well.
The value similarity makes the delta compression effective to reduce the dynamic energy overheads associated with STT-RAM write.
Centralized write buffer design can better utilize the SRAM write buffer.
Our proposed design can achieve 37.4% energy consumption of the SRAM based design, with negligible performance overheads.

## Slide 21
Thank you!