## Slide 1
Many cache sensitive GPU applications have cache contention → low cache efficiency → poor performance
  Smaller L1 cache capacity per thread
1. Cache Contention and Resource Congestion
3.1. CBWT Design Overview
2. Cache Management Schemes
Cache bypassing retains useful cache lines instead of replacing upon cache miss
  Retain useful data → fewer cache misses per thread
  Many active threads → many misses → high demand on NoC to serve misses, i.e. congestion
    Cores may be underutilized due to NoC congestion
  Bypassing still cannot avoid locality loss
Warp throttling temporarily deactivates some threads
  Fewer threads sharing the cache → more cache per thread → fewer cache misses
  Few active threads → cannot hide latency through multithreading
    Cores may be underutilized due to low thread parallelism
  Resource (e.g. NoC bandwidth) under-utilization
3.2. Maximum Active Warps Prediction
Cache contention information is collected by the L2 cache
  Used by predictor to enable/disable bypassing and throttling
Bypass ratio is used to quickly estimate the optimal MAW
  Bypass ratio denotes cache bypass as a fraction of accesses
5. Conclusion
CBWT enables GPGPU for irregular applications from memory hierarchy’s point of view
CBWT significantly outperforms existing management schemes in terms of performance and energy efficiency
The cost-effective CBWT design is more practical to implement in real hardware
  A novel cache contention detection mechanism (leveraging L2 cache’s tag array)
Come to Session 4A in Main Auditorium on Dec. 16 (Tuesday) at 11:10 AM for more details
Extra sampling modules (yellow blocks) are added to monitor contention and congestion
CBWT components:
  Contention detector
  Congestion detector
  CBWT predictor
The victim bits records the access history from a particular L1 cache before the line's eviction
[1] State Key Laboratory of High Performance Computing, National University of Defense Technology, Changsha, China
[2] School of Computer, National University of Defense Technology, Changsha, China
[3] Department of Electrical and Computer Engineering, University of Illinois at Urbana-Champaign, Urbana, USA
Xuhao Chen1,2,3, Li-Wen Chang3, Chris Rodrigues3, Jie Lv3, Zhiying Wang1,2, Wen-Mei Hwu3
Adaptive Cache Management for Energy-efficient GPU Computing
4. Experimental Results
CBWT achieves an average of 74% (maximum 661%) IPC improvement on HCS benchmarks over baseline
  Significantly outperforms PDP bypass (42%) and Best-SWL (52%)
  Due to a sharp reduction in cache misses
  We propose Coordinated Bypassing and Warp Throttling (CBWT) to improve GPU cache efficiency
  Reduce cache contention rate and NoC latency
CBWT outperforms the baseline with an average of 58.6% Perf/Watt improvement
  On average, PDP bypassing can reduce 16.5% of DRAM traffic,
  CBWT reduces DRAM traffic by 54.9%
  CBWT is still beneficial when advanced warp schedulers or larger L1 caches are applied (see paper)
A 2.68x speedup on average (harmonic mean) for highly cache sensitive (HCS) benchmarks
High Contention Rate for HCS benchmarks
NoC latency increases when Maximum Active Warps (MAW) increases
  SWL: Static Wavefront Limiting (warp throttling)
  PDP (Protection Distance Prediction) bypass policy on GPU achieves
  an HCS speedup of 1.57x
NoC latency feedback controls multithreading
  Adjust MAW to keep the network in a busy but low-congestion range
Better than simply combining bypass and warp throttling
  Feedback-driven control on NoC utilization
  Lower hardware overhead
1.84x (SWL+bypass)
1.38x (bypass)
1.46x (SWL)
Proposed L2 cache line
PDP-S: pure cache bypassing Best-SWL: pure warp throttling
MAW=
L1D $ size=