## Slide 1: Architecting Energy-efficient STT-RAM Based Register File on GPGPUs via Delta Compression
Hang Zhang1, Xuhao Chen1, Nong Xiao1,2, Fang Liu1
1State Key Laboratory of High Performance Computing, College of Computer,
National University of Defense Technology, China
2School of Data and Computer Science, Sun Yat-sen University

## Slide 2: Overview
Background
  GPGPU, STT-RAM
Motivation
  Register value similarity on SIMT
Design Details
  delta compression engine
  centralized write buffer
  relaxed retention time
Experimental Evaluation
  performance and energy consumption
Conclusion

## Slide 3: The Processing Engine in Big Data Era
GPGPUs (General Purpose Graphic Processing Unit) have been widely employed
  Deep Learning
  Datacenter
  Supercomputer
“We also implemented a distributed version of AlphaGo that exploited multiple machines, 40 search threads, 1,202 CPUs and 176 GPUs” – Nature, 2016
However, energy-efficiency of GPUs becomes critical
  NVIDIA Tesla P100, 300W
  Intel Core i7-980X Extreme Edition, 130W
Notes: The GPGPU have been widely employed in computing system, thanks to its high throughput and high energy-efficiency for Watt per float point operations,
including deep learning, datacenter, and supercomputer.
2. Google have used 176 GPUs to train the AlphaGO algorithm to beat human GO players.
2. The energy-efficiency of GPU becomes critical for future computing system
.

## Slide 4: GPU Architecture
SIMT architecture: Single Instruction Multiple Threads
  thousands of threads running together
  threads operates on different data
  hiding long memory access latency
  high throughput can be achieved
Register file with large capacity
  save the contexts of threads
  512KB per SM (streaming multiprocessor) on NVIDIA K80 GPU
  constrain how many threads concurrently running
A register read/write operation from a warp
  32 threads / warp
  32 * 32 bit = 1024 bit

## Slide 5: SRAM becomes the energy bottleneck
High leakage SRAM cell
  high leakage power consumption
    escalated leakage power as technology scales
  low density, e.g. 137F2
Energy-efficiency of the register file
  conventionally built with high leakage SRAM
  consume a great portion of GPU total power, 15-20%
  impediment for scaling up GPUs in future generation
6T SRAM

## Slide 6: To combat SRAM leakage
STT-RAM (Spin Transfer Torque magnetic RAM)
  near zero leakage power
  high density, 6-37 F2
  good scalability, 1x nm
  good endurance, 10^15
Building STT-RAM GPU Register File
  R.F. and shared memory [HPCA’13], distributed buffer[DAC’15] , MLC STT-RAM [ASP-DAC’15]
  Goal: make use of near-zero leakage
However, now writing STT-RAM cells becomes a problem
  high write energy consumption
  long write latency

## Slide 7: Our Design Goal
Prior proposals still suffer from
  performance degradation
  high dynamic energy consumption
Our solution
  leverage value similarity in SIMT architecture
  propose a lightweight compression framework to mitigate STT-RAM writes
  redesign a centralized write buffer for better utilization

## Slide 8: Motivation: Register Value Similarity
Value similarity between successive register requests
  many thread-specific local variables, threadID
  some local variables are assigned similar
  input data arrays has a very narrow dynamic range
Register value similarity profiling
1. 79% of the registers are categorized as not random
during non-divergent execution phase
2. Similarity-aware compression algorithm will be effective

## Slide 9: A lightweight compression framework
Base-Delta-Intermediate (BDI) compression
  lightweight: 1 cycle compress/decompression latency
  high compression ratio: when data are similar
    Value similarity on SIMT architecture
The compressed process
  A register value is divided into chunks
  Base: first data chunk
  Delta: difference with base
  Intermediate: chunk data width (2, 4, 8)
STT-RAM writes is reduced
  the number of writes is reduced,
  when data is compressed

## Slide 10: Write driver enhancement
Fine grained write driver control
  32 groups for 1024-bit register entry
  32-bits per group are controlled together
  enable signals are from the compression engine
    control which part of the groups are read/write
Notes: 1. The write driver is redesigned to enable a fine-grained access control on how many of STT-RAM bits can be read/write at the same time.
2. To minimize the control complexity, a bits group of 32-bit is controlled together as a unit.
3. The signals from the compression engine are fed in as the control enabler.

## Slide 11: Centralized Write Buffer
Prior SRAM buffer design
  Each bank has its own write buffer
A
Bank1
Buffer1
Bank2
Buffer2
Bank3
Buffer3
A
B
Bank1
Bank1
Conflict!
Register Requests
Under utilization

## Slide 12: Centralized Write Buffer
Bank1
Buffer1
Bank2
Buffer2
Bank3
Buffer2
A
B
Bank1
Bank1
Register Requests
Buffer
Our proposed design
  A centralized write buffer shared by banks

## Slide 13: Centralized Write Buffer
Buffer
A
B
Our proposed design
  A centralized write buffer shared by banks
Buffer
A
Bank1
Bank2
Bank3
A
B
Bank1
Bank1
Register Requests
Buffer
Centralized writer buffer
  better utilization
  smaller total capacity (SRAM)

## Slide 14: Relaxed retention time STT-RAM cells
Chart: Write Pulse Width (ns)
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0
10 years | 248.2682 | 173.7877 | 148.9609 | 136.5475 | 129.0994 | 124.1341 | 120.5874 | 117.9274 | 115.8585 | 114.2034
1sec | 158.5136 | 110.9595 | 95.1082 | 87.1825 | 82.4271 | 79.2568 | 76.9923 | 75.294 | 73.973 | 72.9163
10ms | 87.6926 | 61.3848 | 52.6156 | 48.2309 | 45.6002 | 43.8463 | 42.5935 | 41.654 | 40.9232 | 40.3386
Write current goes down with reduction in retention time
Retention Time of STT-RAM | Write Latency @ 700Hz
10 Years | 5.5 cycles
1 second | 3 cycles
10 millisecond | 1.5 cycles
Retention Time
10ms retention time equals 7,000,000 cycles on GPUs and is far more than 789 cycles (the average inter-access distance)

## Slide 15: Experimental Evaluation
Hardware Setup
  GPGPUSim simulator
  Nvsim: model STT-RAM
  NVIDIA GTX 480 architecture (Fermi)

## Slide 16: Register File Energy Consumption
Our proposed design consumes only 37.4% register file energy compared to the baseline on average.

## Slide 17: Energy Breakdown
Bar 1 is Base, Bar 2 is WB, Bar 3 is STT+BDI
1.STT-RAM can effectively cut off leakage energy
2. delta compression is good at reducing dynamic energy

## Slide 18: GPU Performance
Our scheme can achieve near 99% performance of the SRAM baseline

## Slide 19: Conclusion
The energy-efficiency of the register file plays a vital role for GPGPU architecture
Leakage problem can be solved by STT-RAM, however, the dynamic energy consumption should be minimized
Delta compression is effective to optimize dynamic energy consumption of STT-RAM based register file.
Centralized write buffer design can improve the utilization of SRAM buffer.
The STT-RAM based register file is promising for future GPU architectures.

## Slide 20
Thank you!
Q&A

## Slide 21: GPGPU Architecture (GTX 480)
ISCA’15 Warped-compression: enabling power efficient GPUs through register compression